Specifications:  Leica TCS SP5 MP confocal microscope

Leica DM 6000 CS upright microscope:

- Full microscope control via color touch-screen

- Spectral confocal detection

- Spectra Physics Mai Tai MP laser

- High speed, high accuracy motorized XYZ stage

- Three confocal detection PMTs, two ND (Non-Descanned) external detectors and one transmitted light detection PMT (for DIC)

- Maximum scanning resolution 4096x4096 pixels

Leica LAS AF software provides:

- Full microscope control (dual LCD displays) for multidimensional series acquisition (x,y,z,t)

- Colocalization (2D and 3D), FRET and FRAP analyses

Brightfield and Differential Interference Contrast (DIC) transmitted light

Epifluorescence with EL 6000 compact lamp and two filter cubes:

- I3	(Blue - Excitation BP 450-490; dichroic mirror 510)

- N2.1	(Green - Excitation BP 515-560; dichroic mirror 580)

Objective Lenses:

- HCX  PL APO CS  10X 0.40 NA	Dry

- HCX  PL APO CS  20X  0.70 NA	Dry

- HCX  PL APO CS   40X 1.25 NA	Oil

- HCX  PL APO CS   63X 1.40 NA	Oil

- HCX  APO L U-V-I  20X 0.50 NA	Water UV

- HCX  APO L U-V-I 40X 0.80 NA	Water

- HCX APO CS 63X 1.20 NA   Water

Acousto Optical Beam Splitter (AOBS)	Acousto Optical Tunable Filter (AOTF)

Lasers:

- Spectra Physics (Mai Tai)	 Tunable 690-1040nm

- Argon/ArKr			458, 478, 488, 514 excitation lines

- HeNe				543 excitation line

- HeNe 				633 excitation line